## Slide 1: WCSA All things Safety
Presented by
Deb Upright
WCSA Director of Coaching

## Slide 2: Introduction
This presentation has been developed to assist all crossbow shooters with knowledge to correctly and safely set up a shooting ground.
This presentation shows the different safety mechanisms of the various crossbows and their correct usage.
This presentation also explains how to check
the safety of all of your equipment and technique.
Enjoy!
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3: Ground Safety
The shooting ground/range must be set up in accordance of the rules of both archery/crossbow governing bodies and council/government laws. Always refer to all the relevant rules. WCSA and the IAU are the world governing bodies for competitive crossbow shooting. Most countries acknowledge either one or the other of these bodies.

## Slide 4: Ground Safety
Flags and signage are a safety necessity. The number and style of each.
are in accordance with the above organisation’s
rules as well as the individual club.
More is always better
Where the public has the right of access, suitable barriers must be erected around the range to keep spectators back.

## Slide 5: Ground Safety
The buttress shall be large enough to accommodate the target face(s) with a minimum of 1cm extra all round the outside the outermost scoring zone(s).
Where conditions warrant it, target buttresses should
be firmly pegged to the ground,
to prevent toppling
or movement.

## Slide 6: Ground Safety
Ideally on the shooting line there should be 1.5m per
shooter, as crossbow limbs can be up to 1m across tip to tip.
A shooter must stay within this allotted space.
Spectators are kept further back than the waiting line
for Target, Indoor and Clout. Generally
spectators are not to be on a field
course.

## Slide 7: Ground Safety
The shoot must be under the direction of one official; usually either a Director of Shooting or a Field Captain/ Range Captain. This official is responsible for the setup, safety and the general running of the shoot.
A shooter must not move forward of the shooting line until authorised
by the DOS or Field Captain / Range Captain,
using either a whistle system or electronic
light and buzzer system, as per rules.

## Slide 8: Ground Safety
Always remembering safety is paramount – so the bow must always face the ground and be pointing down range toward the target, whether loaded or not. Moving to the line
the bow must not be spanned or loaded
and must also face down range. Do not
move about with a loaded crossbow.
A crossbow must only be spanned and loaded when on the shooting line with the exception of an assisted shooter (refer WCSA rules).

## Slide 9: Shooter's Safety
The shooter must check their equipment before
shooting. It is important for the shooter to keep their tackle in good
repair, and fix any issues that may affect their shooting, or the
performance of the bow and bolt.
It is recommended that the fingers of the loading
hand are kept straight and pointing toward the
front of the crossbow, in case of a trigger failure.

## Slide 10: Checking Your Equipment
Safety is always absolute from even before picking up the bow.
It is important that bows, strings, bolts, stringers etc. are regularly checked for wear and are properly maintained.
Don't postpone
Bbbbbbb. Be. any repairs.

## Slide 11: Checking Equipment
Check limbs for possible cracks, splits or abnormalities;
failure to do so can cause a catastrophic outcome.
Check the string for fraying or possible broken strands;
as breaking a string under tension may cause limb damage.
Check the bolt retainer for damage and correct tension.
Check both the trigger and safety mechanisms are working
properly before commencing shooting.

## Slide 12: Checking Equipment
Check that there are no cracks, splits or bulges along the
shafts of the bolts as they could shatter when shot.
Check the shaft behind the point/pile for any damage.
Check the bolt is straight.
Check the nock for sharp nicks and cracks. Replace if needed.
Check for any damage to the point/pile.

## Slide 13: Safety while Spanning a Crossbow
It is very important to span the bow evenly
  Any variation will cause left or right bolt movements, and hence, widening the group.
Only gloves that can be rolled into a ball to fit into the palm of the hand can be worn.
Be sure the foot/feet are firmly pushing on the foot peg/s or stirrup.

## Slide 14: CROSSBOW PARTS - Target
Serving
String
Stock
Trigger
Rear Sight
Butt Hook
Palm Rest
Limbs
Sight
Foot Peg
Rail
Prod Mount
Track
Bolt Retainer
Latch
Cheek Plate
Pre-Set Lever

## Slide 15: CROSSBOW PARTS - SPORTING
Track
Scope
Trigger
Foot Stirrup
Limb
Latch
Bolt
Bolt Retainer
Safety
Stock
Shoulder Strap

## Slide 16: CROSSBOW PARTS - MEDIEVAL
Butt- Tiller
Foot Stirrup
Trigger
Spring Clip - Catch
Prod - Lathe
String

## Slide 17: Terms and Definitions
Bolt – the projectile that is shot. ( A short arrow).
Butt or Tiller – the end of a medieval crossbow that often sits on top of
the shooter's shoulder.
Follow Through – the after shot sequence once the string is released
Loading – the act of placing a bolt onto the bow in such a way that it engages the string.
Palm Rest – forward holding point of the bow.

## Slide 18: Terms and Definitions (continued)
Shouldering the Bow – the way the bow is placed against the shoulder: right shoulder for right handed and left for left handed.
Stirrup – Also known as a foot peg, the place to place the foot to enable
the crossbow to be spanned.
Spanning – the act of evenly raising the string along the track until it clicks onto the "latch" of the trigger mechanism
Stance – the foot position on the ground for best body balance.

## Slide 19: Terms and Definitions (continued)
Track Bow - a crossbow with a channel running along the track upon which the bolt sits and moves
Trackless Bow – a crossbow without a channel but has locating points on the string for the rear of the bolt and a "launcher" at the front so as to support the bolt above the track
Trigger Hand / Finger – the hand and finger used to activate the trigger of the bow.
Triggering / Release – the way in which the trigger of the bow is activated.

## Slide 20: Trigger Safety
As previously stated safety is paramount so understanding
the safety lever system of the bow is imperative.
Some bows have a pre-set lever which is activated before
pulling up the string, so that the string can lock properly onto the latch.
Some have a safety lever that once the string is pulled to the latch the safety lever is activated to SAFE , then the bolt is loaded.
Once the bow is shouldered and while aiming on the
target, the safety is moved to the FIRE position, final
aiming is done and the trigger pulled.

## Slide 21: Loading Safety
Always have the bow facing the target or ground while
loading the bow, in case of a trigger failure.
If loading a track bow, for safety use an open hand and stroking action, the bolt is slid all the way back up the track until it touches the string.
It is important not to curl the fingers because if the trigger fails and the string prematurely releases, injury can occur to your fingers or finger nails.
If using a trackless bow, for safety the bolt must be positively “nocked” or clipped onto the string and the front of the shaft is placed onto a “bolt rest” or launcher.

## Slide 22: Stance Safety
Depending upon a shooters physical make up, the position of the feet may vary, however it is absolutely imperative that at no stage of the shooting process do both feet move forward of the shooting line.

## Slide 23: Shooting Safety
Only point crossbow down range toward the target or at the ground.
Do not swing crossbow into another shooter’s space whether spanned and loaded or not.
Do not move forward until all shooting has ceased and
signal given to score and collect bolts from target.
When placing crossbow at the equipment line
before the shoot begins or between ends, it should
still face down range.

## Slide 24: Storing Crossbow Safety
The transport and storage of the crossbow is not only governed by common sense but also by the local laws of a country’s governing body. If travelling to another country or even another state of the same country, understand what is expected.
Target crossbows generally can be greatly taken apart to store in a case.
Sporting crossbows are usually simply put in a case while strung.

## Slide 25: Summary of Training
This presentation was developed to assist arbalists in being able to set up their gear safely, and shoot safely.
It is also to make arbalists aware of what is regarded as safe when shooting on particular grounds.
Happy safe shooting and may
you always be safe!

## Slide 26: Assessment and Evaluation
Prepare a quiz or challenge to assess how much information participants learned.
Survey participants to see what they found to be beneficial.

## Slide 27: Questions?